Simula Standard - Errata

=====================================================================================

NOTE: Parameter Specification

Simula Standard 5.4.2 states:

specifier
= type [ array | procedure ]
| label
| switch

This is obviously wrong. If we follow the syntax, no-type procedure is illegal, and that was probably not the intention.
No-type array is also not allowed, which inherited from Algol should mean real array.

Simula Common Base 1970 states:

<specifier> ::=
<type> | array | <type> array | label | switch
| procedure	| <type> procedure

Simula Standard should have been changed to:

specifier
= type
| [type] array
| [type] procedure
| label
| switch

=====================================================================================

NOTE: Simula Standard , Chapter 12 Simulation - RANK_IN_SQS

The Simula Standard (under the definition of Class Simulation) states:

        ref (EVENT_NOTICE) procedure pred; pred:- PRED;

        procedure RANK_IN_SQS (afore); Boolean afore;
        begin ref (EVENT_NOTICE) evt;
        evt:- SQS.last;
        while evt.EVTIME > EVTIME do evt :- evt.pred;
        if afore then
        while evt.EVTIME = EVTIME do evt :- evt.pred;
        follow(evt)
        end RANK_IN_SQS;

Here procedure pred is redefined so that 'pred' of the first element is the head itself
and not none like in Simset.

In Simula, this should give 'qua-check failed'.
Which led to 'cast' error in Java.

The procedure RANK_IN_SQS must be rewritten.

NOTE: lowten

Simula Standard (Chapter 9 Class "ENVIRONMENT") states:

character procedure lowten(c); character c;
if ... ! c is illegal as lowten;
  then error("..." ! Lowten error ;)
else begin
lowten:= CURRENTLOWTEN; CURRENTLOWTEN:= c
end lowten;

Changes the value of the current lowten character to that of the
parameter. The previous value is returned. Illegal parameters are
digits, plus ("+"), minus ("-"), dot ("."), comma (","),
control characters (i.e. ISO code<32), DEL (ISO code 127),
and all characters with ISO code greater than 127.

Here, ISO code 32 (SPACE) is indicated as a legal LOWTEN character.

Correct the text to:

Changes the value of the current lowten character to that of the
parameter. The previous value is returned. Illegal parameters are
digits, plus ("+"), minus ("-"), dot ("."), comma (","), space (" "),
control characters (i.e. ISO code<32), DEL (ISO code 127),
and all characters with ISO code greater than 127.

=====================================================================================

Note:

Simula Standard (Chapter 10 Class "INPUT-OUTPUT") states:

The user's main program acts as if it were embedded as follows:

BASICIO (inlength, outlength) Note ! prefixed block;
inspect SYSIN do
inspect SYSOUT do
begin <external-head> <program> end
end prefixed block

The word Note must be replaced by begin

=====================================================================================